## Slide 1: Chapter 13 Embedded Operating Systems
Eighth Edition By William Stallings
Operating Systems: Internals and Design Principles
Notes: “Operating Systems: Internal and Design Principles”, 8/e, by William Stallings, Chapter 13 “Embedded Operating Systems”.

## Slide 2: Embedded System
Refers to the use of electronics and software within a product that is designed to perform a dedicated function
    in many cases, embedded systems are part of a larger system or product
    antilock braking system in a car would be an example
Notes: The term embedded system refers to the use of electronics and software within a
product, as opposed to a general-purpose computer, such as a laptop or desktop
system. The following is a good general definition:
Embedded system : A combination of computer hardware and software, and
perhaps additional mechanical or other parts, designed to perform a dedicated
function. In many cases, embedded systems are part of a larger system or product,
as in the case of an antilock braking system in a car.
Often, embedded systems are tightly coupled to their environment. This can
give rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations.
If multiple activities must be managed simultaneously, this imposes more complex
real-time constraints.

## Slide 3
Notes: Figure 13.1, based on [KOOP96], shows in general terms an embedded system
organization. In addition to the processor and memory, there are a number of elements
that differ from the typical desktop or laptop computer:
• There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment.
• The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision.
• The diagnostic port may be used for diagnosing the system that is being controlled—
not just for diagnosing the embedded computer.
• Special-purpose field programmable (FPGA), application specific (ASIC), or
even nondigital hardware may be used to increase performance or safety.
• Software often has a fixed function and is specific to the application.

## Slide 4: Characteristics of Embedded OS
Real-time operation
Reactive operation
Configurability
I/O device flexibility
Streamlined protection mechanisms
Direct use of interrupts
Notes: A simple embedded system, with simple functionality, may be controlled by a
special-purpose program or set of programs with no other software. Typically,
more complex embedded systems include an OS. Although it is possible in
principle to use a general-purpose OS, such as Linux, for an embedded system,
constraints of memory space, power consumption, and real-time requirements
typically dictate the use of a special-purpose OS designed for the embedded
system environment.
The following are some of the unique characteristics and design requirements
for embedded operating systems:
• Real-time operation: In many embedded systems, the correctness of a computation
depends, in part, on the time at which it is delivered. Often, real-time
constraints are dictated by external I/O and control stability requirements.
• Reactive operation: Embedded software may execute in response to external
events. If these events do not occur periodically or at predictable intervals, the
embedded software may need to take into account worst-case conditions and
set priorities for execution of routines.
• Configurability: Because of the large variety of embedded systems, there is
a large variation in the requirements, both qualitative and quantitative, for
embedded OS functionality. Thus, an embedded OS intended for use on a
variety of embedded systems must lend itself to flexible configuration so that
only the functionality needed for a specific application and hardware suite is
provided. [MARW06] gives the following examples. The linking and loading
functions can be used to select only the necessary OS modules to load.
Conditional compilation can be used. If an object-oriented structure is used,
proper subclasses can be defined. However, verification is a potential problem
for designs with a large number of derived tailored operating systems.
Takada cites this as a potential problem for eCos [TAKA01].
• I/O device flexibility: There is virtually no device that needs to be supported
by all versions of the OS, and the range of I/O devices is large. [MARW06]
suggests that it makes sense to handle relatively slow devices such as disks and
network interfaces by using special tasks instead of integrating their drives into
the OS kernel.
Streamlined protection mechanisms: Embedded systems are typically designed
for a limited, well-defined functionality. Untested programs are rarely added
to the software. After the software has been configured and tested, it can be
assumed to be reliable. Thus, apart from security measures, embedded systems
have limited protection mechanisms. For example, I/O instructions need
not be privileged instructions that trap to the OS; tasks can directly perform
their own I/O. Similarly, memory protection mechanisms can be minimized.
[MARW06] provides the following example. Let switch correspond to the
memory-mapped I/O address of a value that needs to be checked as part of an
I/O operation. We can allow the I/O program to use an instruction such as load
register , switch to determine the current value. This approach is preferable
to the use of an OS service call, which would generate overhead for saving
and restoring the task context.
• Direct use of interrupts: General-purpose operating systems typically do not
permit any user process to use interrupts directly. [MARW06] lists three
reasons why it is possible to let interrupts directly start or stop tasks (e.g., by
storing the task’s start address in the interrupt vector address table) rather than
going through OS interrupt service routines: (1) Embedded systems can be
considered to be thoroughly tested, with infrequent modifications to the OS or
application code; (2) protection is not necessary, as discussed in the preceding
bullet item; and (3) efficient control over a variety of devices is required.

## Slide 5: Developing an Embedded OS
Two general approaches:
take an existing OS and adapt it for the embedded application
design and implement an OS intended solely for embedded use
Notes: There are two general approaches to developing an embedded OS.
  The first approach is to take an existing OS and adapt it for the embedded application.
  The other approach is to design and implement an OS intended solely for embedded use

## Slide 6: Adapting an Existing OS
An existing commercial OS can be used for an embedded system by adding:
    real time capability
    streamlining operation
    adding necessary functionality
Advantage:
familiar interface
Disadvantage:
not optimized for real-time and embedded applications
Notes: An existing commercial OS can be used for an embedded system by adding real time
capability, streamlining operation, and adding necessary functionality. This
approach typically makes use of Linux, but FreeBSD, Windows, and other general purpose
operating systems have also been used. Such operating systems are typically
slower and less predictable than a special-purpose embedded OS. An advantage of
this approach is that the embedded OS derived from a commercial general-purpose
OS is based on a set of familiar interfaces, which facilitates portability.
The disadvantage of using a general-purpose OS is that it is not optimized
for real-time and embedded applications. Thus, considerable modification may be
required to achieve adequate performance. In particular, a typical OS optimizes for
the average case rather than the worst case for scheduling, usually assigns resources
on demand, and ignores most if not all semantic information about an application.

## Slide 7: Purpose-Built Embedded OS
Typical characteristics include:
  fast and lightweight process or thread switch
  scheduling policy is real time and dispatcher module is part of scheduler
  small size
  responds to external interrupts quickly
  minimizes intervals during which interrupts are disabled
  provides fixed or variable-sized partitions for memory management
  provides special sequential files that can accumulate data at a fast rate
Two examples are:
eCos
TinyOS
Notes: A significant number of operating systems have been designed from the ground up
for embedded applications. Two prominent examples of this latter approach are
eCos and TinyOS, both of which are discussed in this chapter.
Typical characteristics of a specialized embedded OS include the following:
• Has a fast and lightweight process or thread switch
• Scheduling policy is real time and dispatcher module is part of scheduler
instead of separate component.
• Has a small size
• Responds to external interrupts quickly; typical requirement is response time
of less than 10 μs
• Minimizes intervals during which interrupts are disabled
• Provides fixed or variable-sized partitions for memory management as well as
the ability to lock code and data in memory
• Provides special sequential files that can accumulate data at a fast rate

## Slide 8: Timing Constraints
To deal with timing constraints, the kernel:
provides bounded execution time for primitives
maintains a real-time clock
provides for special alarms and timeouts
supports real-time queuing disciplines
provides primitives to delay processing by a fixed amount of time and to suspend/resume execution
Notes: To deal with timing constraints, the kernel
• Provides bounded execution time for most primitives
• Maintains a real-time clock
Provides for special alarms and time-outs
• Supports real-time queuing disciplines such as earliest deadline first and
primitives for jamming a message into the front of a queue
• Provides primitives to delay processing by a fixed amount of time and to
suspend/resume execution
The characteristics just listed are common in embedded operating systems with
real-time requirements. However, for complex embedded systems, the requirement
may emphasize predictable operation over fast operation, necessitating different
design decisions, particularly in the area of task scheduling.

## Slide 9: Embedded Linux
A version of Linux running in an embedded system
Embedded devices typically require support for a specific set of devices, periphrals, and protocols, depending on the hardware that is present in a given device and the intended purpose of that device
An embedded Linux distribution is a version of Linux to be customized for the size and hardware constraints of embedded devices
    includes software packages that support a variety of services and applications on those devices
    an embedded Linux kernel will be far smaller than an ordinary Linux kernel
Notes: The term embedded Linux simply means a version of Linux running in an embedded
system. In this section, we highlight some of the key differences between embedded
Linux and a version of Linux running on a desktop or laptop computer.
Desktop and server Linux systems need to support a large number of devices because
of the wide variety of configurations that use Linux. Similarly, such systems
also need to support a range of communication and data exchange protocols so that
they can be used for a large number of different purposes. Embedded devices typically
require support for a specific set of devices, peripherals, and protocols, depending
on the hardware that is present in a given device and the intended purpose of
that device. Fortunately, the Linux kernel is highly configurable in terms of the architecture
that it is compiled for and the processors and devices that it supports.
An embedded Linux distribution is a version of Linux to be customized for
the size and hardware constraints of embedded devices, and includes software packages
that support a variety of services and applications on those devices. Thus, an
embedded Linux kernel will be far smaller than an ordinary Linux kernel.

## Slide 10: Cross Compiler
A key differentiator between desktop/server and embedded Linux distributions is that desktop and server software is typically compiled on the platform where it will execute
Embedded Linux distributions are usually compiled on one platform but are intended to be executed on another
    the software used for this purpose is referred to as a cross-compiler
Notes: A key differentiator between desktop/server and embedded Linux distributions is
that desktop and server software is typically compiled on the platform where it will
execute, while embedded Linux distributions are usually compiled on one platform
but are intended to be executed on another. The software used for this purpose is
referred to as a cross-compiler .

## Slide 11: Embedded Linux File Systems
File system must be as small as possible
Commonly used examples:
  cramfs
      a simple read-only file system that is designed to minimize size by maximizing the efficient use of underlying storage
      files are compressed in units that match the Linux page size
    squashfs
      a compressed, read-only file system that was designed for use on low memory or limited storage size environments
    jffs2
      a log-based file system that is designed for use on NOR and NAND flash devices with special attention to flash-oriented issues such as wear-leveling
    ubifs
      provides better performance on larger flash devices and also supports write caching to provide additional performance inprovements
    yaffs2
      provides a fast and robust file system for large flash devices
Notes: Some applications may create relatively small file systems to be used only for the duration
of the application and which can be stored in main memory. But in general, a
file system must be stored in persistent memory, such as flash memory or traditional
disk-based storage devices. For most embedded systems, an internal or external disk
is not an option, and persistent storage is generally provided by flash memory.
As with other aspects of an embedded Linux system, the file system must be as
small as possible. A number of such compact file systems have been designed for use
in embedded systems. The following are commonly used examples:
• cramfs: The Compressed RAM file system is a simple read-only file system
that is designed to minimize size by maximizing the efficient use of underlying
storage. Files on cramfs file systems are compressed in units that match the
Linux page size (typically 4096 bytes or 4 MB, based on kernel version and
configuration) to provide efficient random access to file contents.
• squashfs: Like cramfs, squashfs is a compressed, read-only file system that was
designed for use on low memory or limited storage size environments such as
embedded Linux systems.
• jffs2: The Journaling Flash File System, version 2, is a log-based file system
that, as the name suggests, is designed for use on NOR and NAND flash devices
with special attention to flash-oriented issues such as wear-leveling.
• ubifs: The Unsorted Block Image File System generally provides better performance
than jffs2 on larger flash devices, and also supports write caching to
provide additional performance improvements.
• yaffs2: Yet another Flash File System, version 2, provides a fast and robust file
system for large flash devices. Yaffs2 requires less RAM to hold file system
state information than file systems such as jffs2, and also generally provides
better performance if the file system is being written to frequently.

## Slide 12: Advantages of Embedded Linux
Advantages of using Linux as the basis for an embedded OS include the following:
  vendor independence
    the platform provider is not dependent on a particular vendor to provide needed features and meet deadlines for deployment
  varied hardware support
    Linux support for a wide range of processor architectures and peripheral devices makes it suitable for virtually any embedded system
  low cost
    the use of Linux minimizes cost for development and training
  open source
    the use of Linux provides all of the advantages of open source software
Notes: Embedded versions of Linux began to appear as early as 1999. A number of companies
have developed their own versions tailored to specific platforms. Advantages of
using Linux as the basis for an embedded OS include the following:
• Vendor independence: The platform provider is not dependent on a particular
vendor to provide needed features and meet deadlines for deployment.
• Varied hardware support: Linux support for a wide range of processor architectures
and peripheral devices makes it suitable for virtually any embedded
system.
• Low cost: The use of Linux minimizes cost for development and training.
• Open source: The use of Linux provides all of the advantages of open source
software.

## Slide 13: Android
Focus of Android lies in the vertical integration of the Linux kernel and the Android user-space components
Many embedded Linux developers do not consider Android to be an instance of embedded Linux
  from the point of view of these developers, a classic embedded device has a fixed function, frozen at the factory
Android
more of a platform OS that can support a variety of applications that vary from one platform to the next
a vertically integrated system, including some Android specific modification to the Linux kernel
an embedded OS based on a Linux kernel
Notes: As we have discussed throughout this book, Android is an embedded OS based on
a Linux kernel. Thus, it is reasonable to consider Android an example of embedded
Linux. However, many embedded Linux developers do not consider Android to be
an instance of embedded Linux [CLAR13]. From the point of view of these developers,
a classic embedded device has a fixed function, frozen at the factory. Android
is more of a platform OS that can support a variety of applications that vary from
one platform to the next. Further, Android is a vertically integrated system, including
some Android-specific modifications to the Linux kernel. The focus of Android
lies in the vertical integration of the Linux kernel and the Android user-space components.
Ultimately, it is a matter of semantics, with no “official” definition of embedded
Linux on which to rely.

## Slide 14: TinyOS
Streamlines to a very minimal OS for embedded systems
Core OS requires 400 bytes of code and data memory combined
Not a real-time OS
There is no kernel
There are no processes
OS doesn’t have a memory allocation system
Interrupt and exception handling is dependent on the peripheral
It is completely nonblocking, so there are few explicit synchronization primitives
Has become a popular approach to implementing wireless sensor network software
Notes: The eCos system provides a more streamlined approach for an embedded OS than
one based on a commercial general-purpose OS, such as an embedded version of
Linux. Thus, eCos and similar systems are better suited for small embedded systems
with tight requirements on memory, processing time, real-time response, power
consumption, and so on. TinyOS takes the process of streamlining to a much further
point, resulting in a very minimal OS for embedded systems. The core OS requires
400 bytes of code and data memory, combined.
TinyOS represents a significant departure from other embedded operating
systems. One striking difference is that TinyOS is not a real-time OS. The reason for
this is the expected workload, which is in the context of a wireless sensor network,
as described in the next subsection. Because of power consumption, these devices
are off most of the time. Applications tend to be simple, with processor contention
not much of an issue.
Additionally, in TinyOS there is no kernel, as there is no memory protection
and it is a component-based OS; there are no processes; the OS itself does not have
a memory allocation system (although some rarely used components do introduce
one); interrupt and exception handling is dependent on the peripheral; and it is
completely nonblocking, so there are few explicit synchronization primitives.
TinyOS has become a popular approach to implementing wireless sensor
network software. Currently, over 500 organizations are developing and contributing
to an open source standard for Tiny OS.

## Slide 15
Notes: TinyOS was developed primarily for use with networks of small wireless sensors. A
number of trends have enabled the development of extremely compact, low-power
sensors. The well-known Moore’s law continues to drive down the size of memory
and processing logic elements. Smaller size in turn reduces power consumption. Low
power and small size trends are also evident in wireless communications hardware,
micro-electromechanical sensors (MEMS), and transducers. As a result, it is possible
to develop an entire sensor complete with logic in a cubic millimeter. The application
and system software must be compact enough that sensing, communication, and computation
capabilities can be incorporated into a complete, but tiny, architecture.
Low–cost, small–size, low-power-consuming wireless sensors can be used in a
host of applications [ROME04]. Figure 13.2 shows a typical configuration. A base
station connects the sensor network to a host PC and passes on sensor data from the
network to the host PC, which can do data analysis and/or transmit the data over
a corporate network or Internet to an analysis server. Individual sensors collect
data and transmit these to the base station, either directly or through sensors that
act as data relays. Routing functionality is needed to determine how to relay the
data through the sensor network to the base station. [BUON01] points out that, in
many applications, the user will want to be able to quickly deploy a large number of
low-cost devices without having to configure or manage them. This means that they
must be capable of assembling themselves into an ad hoc network. The mobility of
individual sensors and the presence of RF interference means that the network will
have to be capable of reconfiguring itself in a matter of seconds.

## Slide 16: TinyOS Goals
With the tiny distributed sensor application in mind, the following goals were set for TinyOS:
  allow high concurrency
  operate with limited resources
  adapt to hardware evolution
  support a wide range of applications
  support a diverse set of platforms
  be robust
Notes: With the tiny, distributed sensor application in mind, a group of researchers from
UC Berkeley [HILL00] set the following goals for TinyOS:
• Allow high concurrency: In a typical wireless sensor network application, the
devices are concurrency intensive. Several different flows of data must be kept
moving simultaneously. While sensor data are input in a steady stream, processed
results must be transmitted in a steady stream. In addition, external
controls from remote sensors or base stations must be managed.
• Operate with limited resources: The target platform for TinyOS will have limited
memory and computational resources and run on batteries or solar power.
A single platform may offer only kilobytes of program memory and hundreds
of bytes of RAM. The software must make efficient use of the available processor
and memory resources while enabling low-power communication.
• Adapt to hardware evolution: Most hardware is in constant evolution; applications
and most system services must be portable across hardware generations.
Thus, it should be possible to upgrade the hardware with little or no software
change, if the functionality is the same.
• Support a wide range of applications: Applications exhibit a wide range of
requirements in terms of lifetime, communication, sensing, and so on. A modular,
general-purpose embedded OS is desired so that a standardized approach
leads to economies of scale in developing applications and support software.
• Support a diverse set of platforms: As with the preceding point, a general purpose
embedded OS is desirable.
• Be robust: Once deployed, a sensor network must run unattended for months
or years. Ideally, there should be redundancy both within a single system and
across the network of sensors. However, both types of redundancy require
additional resources. One software characteristic that can improve robustness
is to use highly modular, standardized software components.
It is worth elaborating on the concurrency requirement. In a typical application,
there will be dozens, hundreds, or even thousands of sensors networked
together. Usually, little buffering is done, because of latency issues. For example,
if you are sampling every 5 minutes and want to buffer four samples before sending,
the average latency is 10 minutes. Thus, information is typically captured, processed,
and streamed onto the network in a continuous flow. Further, if the sensor
sampling produces a significant amount of data, the limited memory space available
limits the number of samples that could be buffered. Even so, in some applications,
each of the flows may involve a large number of low-level events interleaved with
higher-level processing. Some of the high-level processing will extend over multiple
real-time events. Further, sensors in a network, because of the low power of transmission
available, typically operate over a short physical range. Thus data from outlying
sensors must be relayed to one or more base stations by intermediate nodes.

## Slide 17: TinyOS Components
Embedded software systems built with TinyOS consist of a set of modules (called components), each of which performs a simple task and which interface with each other and with hardware in limited and well-defined ways
The only other software module is the scheduler
Because there is no kernel there is no actual OS
The application area of interest is the wireless sensor network (WSN)
Examples of standardized components include:
single-hop networking
ad-hoc routing
power management
timers
nonvolatile storage control
Notes: An embedded software system built using TinyOS consists of a set of small modules,
called components, each of which performs a simple task or set of tasks and which
interface with each other and with hardware in limited and well-defined ways. The
only other software module is the scheduler, discussed subsequently. In fact, because
there is no kernel, there is no actual OS. But we can take the following view. The application
area of interest is the wireless sensor network (WSN). To meet the demanding
software requirements of this application, a rigid, simplified software architecture
is dictated, consisting of components. The TinyOS development community has
implemented a number of open-source components that provide the basic functions
needed for the WSN application. Examples of such standardized components include
single-hop networking, ad-hoc routing, power management, timers, and nonvolatile
storage control. For specific configurations and applications, users build additional
special-purpose components and link and load all of the components needed for the
user’s application. TinyOS, then, consists of a suite of standardized components. Some
but not all of these components are used, together with application-specific user-written
components, for any given implementation. The OS for that implementation is simply
the set of standardized components from the TinyOS suite.

## Slide 18
Notes: All components in a TinyOS configuration have the same structure, an example
of which is shown in Figure 13.3a . The shaded box in the diagram indicates
the component, which is treated as an object that can only be accessed by defined
interfaces, indicated by white boxes. A component may be hardware or software.
Software components are implemented in nesC, which is an extension of C with
two distinguishing features: a programming model where components interact via
interfaces, and an event-based concurrency model with run-to-completion task and
interrupt handlers, explained subsequently.
The architecture consists of a layered arrangement of components. Each component
can link to only two other components, one below it in the hierarchy and one
above it. A component issues commands to its lower-level component and receives
event signals from it. Similarly, the component accepts commands from its upper-level
component and issues event signals to it. At the bottom of the hierarchy are hardware
components and at the top of the hierarchy are application components, which may
not be part of the standardized TinyOS suite but which must conform to the TinyOS
component structure.

## Slide 19: Components -- Tasks
A software component implements one or more tasks
Each task in a component is similar to a thread in an ordinary OS
Within a component tasks are atomic
    once a task has started it runs to completion
A task cannot:
be preempted by another task in the same component and there is no time slicing
block or spin wait
A task can:
perform computations
call lower-level components (commands)
signal higher-level events
schedule other tasks
Notes: A software component implements one or more tasks. Each task in a component
is similar to a thread in an ordinary OS, with certain limitations. Within a component,
tasks are atomic: Once a task has started, it runs to completion. It cannot
be preempted by another task in the same component, and there is no time slicing.
However, a task can be preempted by an event. A task cannot block or spin wait.
These limitations greatly simplify the scheduling and management of tasks within
a component. There is only a single stack, assigned to the currently running task.
Tasks can perform computations, call lower-level components (commands) and signal
higher-level events, and schedule other tasks.

## Slide 20: Components -- Commands
A command is a nonblocking request
    a task that issues a command does not block or spin wait for a reply from the lower-level component
Is typically a request for the lower-level component to perform some service
The effect on the component that receives the command is specific to the command given and the task required to satisfy the command
A command cannot preempt the currently running task
A command does not cause a preemption in the called component and does not cause blocking in the calling component
Notes: Commands are nonblocking requests. That is, a task that issues a command
does not block or spin wait for a reply from the lower-level component. A command
is typically a request for the lower-level component to perform some service,
such as initiating a sensor reading. The effect on the component that receives the
command is specific to the command given and the task required to satisfy the command.
Generally, when a command is received, a task is scheduled for later execution,
because a command cannot preempt the currently running task. The command
returns immediately to the calling component; at a later time, an event will signal
completion to the calling component. Thus, a command does not cause a preemption
in the called component and does not cause blocking in the calling component.

## Slide 21: Components -- Events
Events in TinyOS may be tied either directly or indirectly to hardware events
Lowest-level software components interface directly to hardware interrupts
    may be external interrupts, timer events, or counter events
An event handler in a lowest-level component may handle the interrupt itself or may propagate event messages up through the component hierarchy
A command can post a task that will signal an event in the future
    in this case there is no tie of any kind to a hardware event
Notes: Events in TinyOS may be tied either directly or indirectly to hardware events.
The lowest–level software components interface directly to hardware interrupts,
which may be external interrupts, timer events, or counter events. An event handler in
a lowest-level component may handle the interrupt itself or may propagate event messages
up through the component hierarchy. A command can post a task that will signal
an event in the future. In this case, there is no tie of any kind to a hardware event.

## Slide 22
Notes: Components are organized into configurations by “wiring” them together at
their interfaces and equating the interfaces of the configuration with some of the interfaces
of the components. A simple example is shown in Figure 13.3b . The uppercase
C stands for Component. It is used to distinguish between an interface (e.g., Timer)
and a component that provides the interface (e.g., TimerC).The uppercase M stands
for Module. This naming convention is used when a single logical component has both
a configuration and a module. The TimerC component, providing the Timer interface,
is a configuration that links its implementation (TimerM) to Clock and LED providers.
Otherwise, any user of TimerC would have to explicitly wire its subcomponents.

## Slide 23: TinyOS Scheduler
Operates across all components
Only one task executes at a time
The scheduler is a separate component
    it is the one portion of TinyOS that must be present in any system
Default scheduler is a simple FIFO queue
Scheduler is power aware
  puts processor to sleep when there is no task in the queue
Notes: The TinyOS scheduler operates across all components. Virtually all embedded systems
using TinyOS will be uniprocessor systems, so that only one task among all
the tasks in all the components may execute at a time. The scheduler is a separate
component. It is the one portion of TinyOS that must be present in any system.
The default scheduler in TinyOS is a simple FIFO (first-in-first-out) queue. A task
is posted to the scheduler (place in the queue) either as a result of an event, which triggers
the posting, or as a result of a specific request by a running task to schedule another
task. The scheduler is power aware. This means that the scheduler puts the processor to
sleep when there are no tasks in the queue. The peripherals remain operating, so that
one of them can wake up the system by means of a hardware event signaled to a lowest level
component. Once the queue is empty, another task can be scheduled only as a
result of a direct hardware event. This behavior enables efficient battery usage.
The scheduler has gone through two generations. In TinyOS 1.x, there is a shared
task queue for all tasks, and a component can post a task to the scheduler multiple
times. If the task queue is full, the post operation fails. Experience with networking
stacks showed this to be problematic, as the task might signal completion of a splitphase
operation: If the post fails, the component above might block forever, waiting
for the completion event. In TinyOS 2.x, every task has its own reserved slot in the
task queue, and a task can only be posted once. A post fails if and only if the task has
already been posted. If a component needs to post a task multiple times, it can set
an internal state variable so that when the task executes, it reposts itself. This slight
change in semantics greatly simplifies a lot of component code. Rather than test to
see if a task is posted already before posting it, a component can just post the task.
Components do not have to try to recover from failed posts and retry. The cost is one
byte of state per task.
A user can replace the default scheduler with one that uses a different
dispatching scheme, such as a priority-based scheme or a deadline scheme. However,
preemption and time slicing should not be used because of the overhead such systems
generate. More importantly, they violate the TinyOS concurrency model, which
assumes tasks do not preempt each other.

## Slide 24
Notes: Figure 13.4 shows a configuration assembled from software and hardware components.
This simplified example, called Surge and described in [GAY03], performs periodic sensor sampling and
uses ad-hoc multihop routing over the wireless network
to deliver samples to the base station. The upper part of the figure shows the
components of Surge (represented by boxes) and the interfaces by which they are
wired (represented by arrowed lines). The SurgeM component is the application level
component that orchestrates the operation of the configuration.
Figure 13.4b shows a portion of the configuration for the Surge application.
This example illustrates the strength of the TinyOS approach. The software is
organized as an interconnected set of simple modules, each of which defines one or
a few tasks. Components have simple, standardized interfaces to other components,
be they hardware or software. Thus, components can easily be replaced. Components
can be hardware or software, with a boundary change not visible to the application
programmer.

## Slide 25: TinyOS Resource Interface
TinyOS provides a simple but powerful set of conventions for dealing with resources
Dedicated
a resource that a subsystem needs exclusive access to at all times
no sharing policy is needed
examples include interrupts and counters
Virtualized
every client of a virtualized resource interacts with it as if it were a dedicated resource
an example is a clock or timer
Shared
abstraction that provides access to a dedicated resource through an arbiter component
arbiter determines which client has access to the resource at which time
Notes: TinyOS provides a simple but powerful set of conventions for dealing with resources.
Three abstractions for resources are used in TinyOS:
• Dedicated: A resource that a subsystem needs exclusive access to at all times. In
this class of resources, no sharing policy is needed since only a single component
ever requires use of the resource. Examples of dedicated abstractions include
interrupts and counters.
• Virtualized: Every client of a virtualized resource interacts with it as if it were a
dedicated resource, with all virtualized instances being multiplexed on top of a
single underlying resource. The virtualized abstraction may be used when the
underlying resource need not be protected by mutual exclusion. An example
is a clock or timer.
• Shared: The shared resource abstraction provides access to a dedicated
resource through an arbiter component. The arbiter enforces mutual exclusion,
allowing only one user (called a client) at a time to have access to a resource
and enabling the client to lock the resource.
In the remainder of this subsection, we briefly define the shared resource
facility of TinyOS. The arbiter determines which client has access to the resource
at which time. While a client holds a resource, it has complete and unfettered control.
Arbiters assume that clients are cooperative, only acquiring the resource when
needed and holding on to it no longer than necessary. Clients explicitly release
resources: There is no way for an arbiter to forcibly reclaim it.

## Slide 26
Notes: Figure 13.5 shows a simplified view of the shared resource configuration used to
provide access to an underlying resource. Associated with each resource to be shared
is an arbiter component. The arbiter enforces a policy that enables a client to lock
the resource, use it, and then release the resource. The shared resource configuration
provides the following interfaces to a client:
• Resource: The client issues a request at this interface, requesting access to the
resource. If the resource is currently locked, the arbiter places the request in a
queue. When a client is finished with the resource, it issues a release command
at this interface.
• Resource requested: This is similar to the Resource interface. In this case, the
client is able to hold on to a resource until the client is notified that someone
else needs the resource.
• Resource configure: This interface allows a resource to be automatically
configured just before a client is granted access to it. Components providing
the ResourceConfigure interface use the interfaces provided by an underlying
dedicated resource to configure it into one of its desired modes of
operation.
• Resource-specific interfaces: Once a client has access to a resource, it uses
resource-specific interfaces to exchange data and control information with the
resource.
In addition to the dedicated resource, the shared resource configuration consists
of two components. The Arbiter accepts requests for access and configuration
from a client and enforces the lock on the underlying resource. The shared resource
component mediates data exchange between the client and the underlying resource.
Arbiter information passed from the arbiter to the shared resource component controls
the access of the client to the underlying resource.

## Slide 27: Summary
Embedded systems
Characteristics of embedded operating systems
  Adapting an existing commercial operating system
  Purpose-built embedded operating system
Embedded Linux
  Kernel size
  Compilation
  Embedded Linux file systems
  Advantages of embedded Linux
  Android
TinyOS
  Wireless sensor networks
  TinyOS goals
  TinyOS components
  TinyOS scheduler
  TinyOS resource interface
Notes: Chapter 13 Summary